## Slide 1
NETWORK TEST INFRASTRUCTURE
The DMVPN Lab Testbed
A three-router Cisco DMVPN network, its hosts and its management server, running as virtual machines on a single Linux box — rebuilt from nothing and re-verified on demand.
215 automated tests across 23 suites, in 24 minutes
PLATFORM
Cisco Catalyst 8000V
IOS-XE 17.15.06
HYPERVISOR
QEMU 10.2 / KVM
7 VMs, one host
HARNESS
Robot Framework 7.3
Python 3.14 · pyATS · Genie

## Slide 2
What the lab is, in one slide
A production-shaped network that can be destroyed and rebuilt without touching production
7
virtual machines
23
test suites
215
automated tests
24 min
full regression
Real software, not a simulator
The routers run the same IOS-XE image as the physical fleet. Behaviour that depends on the operating system — timers, refusals, silent failures — shows up here.
Rebuilt from source config
Ten provisioning phases take a factory-fresh image to a fully configured network. Nothing is hand-typed, so nothing is unrepeatable.
Evidence, not assertions
Every run archives device state, logs and a numbered PDF report. A claim that something passed is backed by the command output that proved it.
Why it matters commercially
Changes to encryption, routing policy, NAT or authentication can be proven safe before they reach a customer site — and a failure found here costs a 24-minute re-run rather than a change window and a truck roll.

## Slide 3
One Linux host carries the whole lab
No dedicated hardware, no cloud spend, no lab booking
THE HOST
CPU
12 cores, KVM accelerated
MEMORY
57 GB total
STORAGE
732 GB (36 GB used)
HYPERVISOR
QEMU 10.2.1, -cpu host
GUEST ACCESS
/dev/kvm, no root needed
How the 57 GB is spent
VIRTUAL MACHINE
IMAGE
CPU
RAM
R1 hub router
Catalyst 8000V
4 vCPU
8,192 MB
R2 spoke router
Catalyst 8000V
4 vCPU
8,192 MB
R3 spoke router
Catalyst 8000V
4 vCPU
8,192 MB
NMS management server
Ubuntu 24.04
1 vCPU
1,024 MB
H1 / H2 / H3 end hosts
CirrOS 0.6.2
1 vCPU
256 MB each
Total committed
25.8 GB
The one real constraint
Two labs of this size cannot run at once — 25.8 GB each against 57 GB. The DMVPN and VTI labs alternate.

## Slide 4
The network under test
Hub-and-spoke DMVPN over a shared WAN, with an out-of-band management plane
WAN 100.64.0.0/24
R1
hub
AS 65001
100.64.0.1
R2
spoke
AS 65002
100.64.0.2
R3
spoke
AS 65003
100.64.0.3
DMVPN overlay Tunnel0 172.20.0.0/24
mGRE + IPsec + NHRP · eBGP over the tunnel
Spokes register with the hub, then build direct spoke-to-spoke tunnels on demand
H1
192.168.10.0/24
H2
192.168.20.0/24
H3
192.168.30.0/24
OOB management 192.168.99.0/24
VRF MGMT on every router
NMS · 192.168.99.10

## Slide 5
How a router VM is started
One shell script, one QEMU process, no hypervisor GUI and no orchestration layer
1
Copy-on-write disk
qemu-img creates a thin overlay backed by the shared 1.9 GB c8000v image. Each router gets a private disk; the golden image is never written to.
2
Day-0 configuration ISO
Hostname, credentials and management addressing are burned to a small ISO and attached as a CD-ROM. IOS-XE reads it only when NVRAM is empty — a genuinely fresh boot.
3
Network interfaces
Four virtio NICs: a user-mode NAT link for the harness, plus WAN, LAN and OOB attached to shared multicast segments.
4
Launch under KVM
-machine pc,accel=kvm -cpu host -smp 4 -m 8192, daemonized with a PID file. Serial console is exposed over telnet for boot-time diagnosis.
5
Wait for readiness
The harness polls the forwarded SSH port until the device answers and settles, rather than sleeping a fixed interval.
start-vm.sh — the essential flags
qemu-system-x86_64 \
-machine pc,accel=kvm \
-cpu host -smp 4 -m 8192 \
-drive if=virtio,file=run/R1.qcow2 \
-drive if=ide,media=cdrom,\
file=run/R1-day0.iso \
# harness reaches the device here
-netdev user,id=mgmt,\
hostfwd=tcp:127.0.0.1:2221-:22 \
# shared L2 segments between VMs
-netdev socket,id=wan,\
mcast=230.10.64.1:10064 \
-netdev socket,id=lan,... \
-netdev socket,id=oob,... \
-serial telnet:127.0.0.1:5001 \
-display none -daemonize

## Slide 6
How the virtual machines are wired together
There is no virtual switch — QEMU multicast sockets act as shared network segments
The problem
A point-to-point socket connects exactly two VMs, which is fine for a back-to-back link but wrong for a shared segment. Three routers on one WAN, or a router and its host on a LAN, need every frame to reach every member — including broadcast and multicast, which NHRP and routing protocols rely on.
The mechanism
Each segment is a multicast group on the loopback interface. Every VM attached to that group sees every frame, exactly like a hub. Pinning to 127.0.0.1 keeps all lab traffic inside the host — nothing reaches the physical network.
SEGMENT
SUBNET
TRANSPORT
MEMBERS
WAN
100.64.0.0/24
mcast 230.10.64.1
R1, R2, R3
LAN per site
192.168.10/20/30.0/24
mcast 230.10.x0.1
one router + its host
OOB management
192.168.99.0/24
mcast 230.10.99.1
R1, R2, R3, NMS
Harness access
10.0.2.0/24
user-mode NAT, hostfwd
each VM, individually
SSH on 2221-2223 reaches the routers, 2231-2233 the hosts, 2241 the NMS — every device addressable from the harness.

## Slide 7
From factory image to configured network
Ten ordered phases, each idempotent and independently re-runnable
1
license
Boot level + reload
2
dmvpn
mGRE, IPsec, NHRP
3
bgp
eBGP, MD5, BFD, policy
4
nat
Static + dynamic pools
5
ntp
Time sync via OOB
6
syslog
Export to NMS
7
snmp
v3 authPriv + traps
8
aaa
TACACS+ authentication
9
vty
Line access control
10
banner
Pre-login notice
Why the licence phase comes first
The cryptographic CLI does not exist until the boot level is active, and the boot level only takes effect on reload.
Teardown and configuration are applied separately
Removing an object that is not there is a harmless no-op; a rejected configuration line is a fault worth stopping for.

## Slide 8
What the network actually does
Every feature below is configured by the harness and verified by it
Overlay & encryption
Multipoint GRE with IPsec protection, IKEv2 with a wildcard keyring, NHRP registration and Phase 3 shortcut switching between spokes.
Routing & policy
eBGP across the tunnel with MD5 authentication and BFD. Outbound prefix-lists, community tagging, inbound community and AS-path filtering, maximum-prefix limits.
Address translation
Static one-to-one mappings and a dynamic pool with overload, including pool exhaustion behaviour under deliberate pressure.
Management plane
A dedicated out-of-band network in VRF MGMT carrying NTP, syslog and SNMPv3 authPriv polling and traps to the NMS.
Identity & access
TACACS+ authentication against a real server, per-line access control, and a pre-login banner verified on every device.
Failure behaviour
Hub loss, underlay partition, key mismatches, MTU blackholes and cache expiry — what the design does when something breaks.
The management, identity and failure work is what turns a connectivity demo into something an operations team can rely on.

## Slide 9
How a test run works
One command, driven entirely over SSH — the same interface an engineer would use
1
./run-tests.sh
Loads lab.env and passes every address, port and credential to the test runner as a variable.
2
Robot Framework
Executes 23 suites in order. Shared keywords live in a resource file; Python libraries handle SNMP, NETCONF and NAT.
3
SSH driver
A reload-safe client opens a session per device, detects the prompt, and distinguishes a real refusal from a benign notice.
4
Devices & NMS
Commands run on the live routers, hosts and management server. Nothing is mocked or replayed.
5
Archive & report
State captures, logs, a numbered evidence PDF and the topology diagram are written to a timestamped folder.
Design rules
• Wait for a condition, never sleep a fixed interval
• Assert on behaviour, not on configuration text
• Every destructive test restores what it broke
• Restoration ends when traffic moves again, not when config returns
• Probe the device before writing the assertion

## Slide 10
The 23 suites
215 tests, every one passing on the reference run of 8 September 2026
01
Platform
5
02
Configuration
5
03
WAN
6
04
DMVPN
13
05
Capture state
12
06
Wire encryption
3
07
IPsec negative
3
08
Management API
6
09
BGP
26
10
Host to host
10
11
Throughput
3
12
NAT
10
13
NAT pool
13
14
NTP
12
15
Syslog
10
16
SNMPv3
13
17
SNMP polling
14
18
MTU
8
19
Out of band
9
20
TACACS+
12
21
VTY ACL
9
22
Banner
6
23
Destructive
7
215 / 215
24.2 minutes, end to end
BGP is the largest suite at 26 tests, because routing policy has the most ways to be quietly wrong: a community that is not stripped, an AS-path filter that permits what it should drop, a prefix-list that never matches.

## Slide 11
The technology stack
Open source throughout, except the router image itself
Virtualisation
QEMU
10.2.1
KVM
hardware accel
virtio-net
guest NICs
cloud-init
NMS + host seed
Network operating system
Catalyst 8000V
IOS-XE 17.15.06
CirrOS
0.6.2 end hosts
Ubuntu
24.04 minimal, NMS
Test harness
Robot Framework
7.3.2
Python
3.14.4
Paramiko / SSHLibrary
device sessions
pyATS + Genie
26.8, parsers
Protocol tooling
pysnmp
7.1.22
ncclient
0.7.1, NETCONF
requests
2.34, RESTCONF
reportlab
5.0.1, reports
Management services
rsyslog
log collection
snmptrapd
trap receiver
chrony
NTP server
tac_plus
TACACS+ server
Reporting
Robot log + report
HTML
Evidence PDF
numbered, per test
Topology PDF
generated diagram
Headless Chrome
HTML to PDF

## Slide 12
What every run leaves behind
A timestamped archive, so any past result can be re-examined rather than recalled
Numbered evidence PDF
Each of the 215 tests appears as a numbered entry — 23.01, 23.02 and so on — with its setup, acceptance criteria, the commands that checked it, and its teardown.
Device state captures
Running configuration, routing and BGP tables, crypto sessions, NAT translations, NTP and SNMP state, taken from every router at the same point in the run.
Management server evidence
Syslog received, SNMP polling output and trap records, collected from the NMS rather than from the device that claims to have sent them.
Robot log and report
Every command and its output, keyword by keyword, for any test that needs to be understood after the fact.
Evidence over recollection
The archive is what lets a result be challenged. Twice this month a suite was found to be passing for the wrong reason — both times by reading the evidence, not by watching a test fail.
One run kept in version control
The repository carries the latest full run as its reference. When the code changes, that archive is regenerated — so the published evidence always matches the tests that produced it.

## Slide 13
Breaking it on purpose
Seven tests that take the fabric apart while traffic is running, and assert what is still standing
Hub loss
The direct spoke-to-spoke tunnel survives — but the routing that used it does not.
Hub recovery
Registration, BGP and the shortcut all return with no operator action.
Underlay partition
Spokes that cannot reach each other fall back through the hub.
NHRP key mismatch
Registration is refused outright.
Tunnel key mismatch
Silently discarded — the interface still reports itself up.
MTU blackhole
Suppress the too-big message and large traffic fails with no diagnostic.
Cache expiry
Shortcuts are soft state and age out when traffic stops justifying them.
The finding that changed a test
Losing the hub was expected to prove resilience. Probing showed the opposite half is also true: the tunnel survives, but both spokes learn routes only from the hub, so the prefixes withdraw and the healthy tunnel carries nothing. Written as a resilience claim, the test would have passed while saying something false.

## Slide 14
What the work has caught so far
The defects that matter most were in the tests, not in the network
An assertion that could not fail
Two shared keywords proving a ping was lossless checked for the text "0% packet loss" — which is contained in "100% packet loss", and in "20% packet loss". They accepted any loss ending in a zero, across 16 call sites in three suites. Now anchored and fixed in both labs.
A teardown that finished too early
Destructive tests restored the configuration and waited for the tunnel to register — but BGP rides that tunnel and needs about a minute more. Later tests began against a network that looked healthy and carried nothing. Teardowns now wait for traffic to move.
A control that never applied
An outbound access list was meant to block the router's "fragmentation needed" message. Outbound lists do not filter traffic the router originates, so it did nothing. The message is now suppressed at its source, which is also the more realistic fault.
A test suite is itself software, and it needs the same scepticism as the network it measures.

## Slide 15
WHERE IT STANDS
Ready to use, and honest about its limits
Both labs are in version control with their reference runs. The DMVPN lab is current and fully green; the VTI lab carries one fix that has not yet been exercised against hardware.
COMPLETE
DMVPN lab: 215 / 215 passing
Destructive coverage: 7 scenarios
Evidence PDF numbered and structured
Both repositories pushed
OPEN
VTI lab fix committed but not re-run
Two labs cannot run at once — 25.8 GB each
Reference archive is ~86 MB per swap
NEXT
Bring the VTI lab up and re-verify
Decide whether raw run data stays in git
Extend destructive coverage to the VTI design
Cisco Catalyst 8000V DMVPN testbed · 8 September 2026
215 tests · 23 suites · 24 minutes